## Slide 1: IB Physics: Chapter 1
Lesson 5b: Uncertainty on graphs

## Slide 2: Uncertainty and Graphs
On graphs we use “Uncertainty Bars” (sometimes called error bars) to display uncertainty.
You simply plot your point, then draw a line (vertically or horizontally) through the point extending the length of twice your uncertainty (One uncertainty up (+) and once uncertainty down (-).
The above uncertainty bar uses an explantion assuming an data point of “25±3”

## Slide 3
Chart: Graph of Period vs Square Root Length for a Simple Pendulum
| 2.2360679774997898 | 3.1622776601683795 | 3.872983346207417 | 4.4721359549995796 | 5 | 5.4772255750516612 | 5.9160797830996161 | 6.324555320336759 | 6.7082039324993694 | 7.0710678118654755
 | 4.5275 | 6.2853 | 7.6251 | 8.5235 | 9.6144 | 10.7734 | 11.4737 | 12.2514 | 13.3856 | 14.2557
Plus Slope | 4.3305 | 15.0897
Minus Slope | 4.7246 | 13.4216
Example of uncertainty bar

## Slide 4: Uncertainty in Slope
When getting the slope of a line, you must draw three lines.
  The first is simply the best fit line.
  The second goes is the “Max” slope.
    Try to draw the steepest slope you can that respects the uncertainty bars, if you can, go from the lowest uncertainty bar on the first data point to the highest uncertainty bar on the last data point.
  The third is the “Min” slope.
    Try to draw that least slope you can that respects the data. Try to go from the highest uncertainty bar on your first data point and the lowest uncertainty bar on your last data point (this is your “min slope”).
You then determine all three slopes.

## Slide 5
Chart: Graph of Period vs Square Root Length for a Simple Pendulum
| 2.2360679774997898 | 3.1622776601683795 | 3.872983346207417 | 4.4721359549995796 | 5 | 5.4772255750516612 | 5.9160797830996161 | 6.324555320336759 | 6.7082039324993694 | 7.0710678118654755
 | 4.2782 | 6.265 | 7.8988 | 8.5132 | 9.7498 | 11.07 | 11.8348 | 12.6026 | 13.3948 | 13.9539
Plus Slope | 4.0873 | 14.9437
Minus Slope | 4.469 | 12.964

## Slide 6: Uncertainty in Slope
In the example on the previous slide the Line of Best fit is: y=2.0129x - 0.157
  The max Slope is: y=2.454x- 0.9335
  The min Slope is: y=1.757x+ 0.5403
To get the uncertainty in slope we divide the range between the max and min slopes by 2.
  Max Slope- Min slope=
  2.454-1.757=0.697
  Our uncertainty becomes 0.3
  2.0 ± 0.3 (round uncertainty to 1 SF)
We could do the same for intercept but that gives us an intercept of 0.2 ± 0.8… By looking at the graph we can see that in all likely hood the intercept is “0”.
So the equation becomes
  y=(2.0 ± 0.3)x